## Slide 1
Chapter 1
Boolean Logic

## Slide 2: Chapter 1: Boolean logic
  Boolean logic
  Boolean function synthesis
  Hardware description language
  Hardware simulation
  Multi-bit buses
  Project 1 overview

## Slide 3: Boolean Values
F T
N Y
0 1

## Slide 4: Boolean Operations

## Slide 5: Boolean Operations
x | y | And
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
And
x And y

## Slide 6: Boolean Operations
x And y x Or y
x | y | And
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
And
x | y | Or
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 7: Boolean Operations
x And y x Or y Not(x)
x | y | And
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
And
x | y | Or
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | Not
0 | 1
1 | 0

## Slide 8: Boolean Expressions
Not(0 Or (1 And 1)) =
Not(0 Or 1) =
Not(1) =
__________

## Slide 9: Boolean Functions
f(x, y, z) = (x And y) Or (Not(x) And z)

## Slide 10: Boolean Functions
f(x, y, z) = (x And y) Or (Not(x) And z)
f
x | y | z | f
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 11: Boolean Functions
f(x, y, z) = (x And y) Or (Not(x) And z)
f
(0 And 0) Or (Not(0) And 1) =
0 Or (1 And 1) =
0 Or 1 = 1
x | y | z | f
0 | 0 | 0 | 
0 | 0 | 1 | 1
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 12: Boolean Functions
f(x, y, z) = (x And y) Or (Not(x) And z)
x | y | z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
f

## Slide 13: Boolean Functions
f(x, y, z) = (x And y) Or (Not(x) And z)
x | y | z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
f
formula
truth table

## Slide 14: Boolean Identities
(x And y) = (y And x)
(x Or y) = (y Or x)
(x And (y And z)) = ((x And y) And z)
(x Or (y Or z)) = ((x Or y) Or z)
(x And (y Or z)) = (x And y) Or (x And z)
(x Or (y And z)) = (x Or y) And (x Or z)
Not(x And y) = Not(x) Or Not(y)
Not(x Or y) = Not(x) And Not(y)
commutative laws (교환법칙)
associative
laws (결합법칙)
distributive
laws (분배법칙)
De Morgan laws

## Slide 15: Boolean Algebra
Not(Not(x) And Not(x Or y)) =

## Slide 16: Boolean Algebra
De Morgan law
Not(Not(x) And Not(x Or y)) =
Not(Not(x) And (Not(x) And Not(y))) =

## Slide 17: Boolean Algebra
associative law
Not(Not(x) And Not(x Or y)) =
Not(Not(x) And (Not(x) And Not(y))) =
Not((Not(x) And Not(x)) And Not(y)) =

## Slide 18: Boolean Algebra
idempotence
(멱등법칙)
Not(Not(x) And Not(x Or y)) =
Not(Not(x) And (Not(x) And Not(y))) =
Not((Not(x) And Not(x)) And Not(y)) =
Not(Not(x) And Not(y)) =

## Slide 19: Boolean Algebra
De Morgan law
Not(Not(x) And Not(x Or y)) =
Not(Not(x) And (Not(x) And Not(y))) =
Not((Not(x) And Not(x)) And Not(y)) =
Not(Not(x) And Not(y)) =
Not(Not(x)) Or Not(Not(y)) =

## Slide 20: Boolean Algebra
Not(Not(x) And Not(x Or y)) =
Not(Not(x) And (Not(x) And Not(y))) =
Not((Not(x) And Not(x)) And Not(y)) =
Not(Not(x) And Not(y)) =
Not(Not(x)) Or Not(Not(y)) =
x Or y
double negation

## Slide 21: Boolean Algebra
Not(Not(x) And Not(x Or y)) =

## Slide 22: Boolean Algebra
Not(Not(x) And Not(x Or y)) =
x | y | Or
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 23: Boolean Algebra
Not(Not(x) And Not(x Or y)) =
________
x | y | Or
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 24: Chapter 1: Boolean logic
  Boolean logic
  Boolean function synthesis
  Hardware description language
  Hardware simulation
  Multi-bit buses
  Project 1 overview

## Slide 25: Boolean expression  truth table
f(x, y, z) = (x And y) Or (Not(x) And z)
x | y | z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 26: Boolean expression  truth table
f(x, y, z) = (x And y) Or (Not(x) And z)
x | y | z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
?

## Slide 27: From truth table to a Boolean expression
x | y | z | f
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 28: From truth table to a Boolean expression
(Not(x) And Not(y) And Not(z))
x | y | z | f
0 | 0 | 0 | 1 1
0 | 0 | 1 | 0 0
0 | 1 | 0 | 1 0
0 | 1 | 1 | 0 0
1 | 0 | 0 | 1 0
1 | 0 | 1 | 0 0
1 | 1 | 0 | 0 0
1 | 1 | 1 | 0 0

## Slide 29: From truth table to a Boolean expression
(Not(x) And y And Not(z))
x | y | z | f
0 | 0 | 0 | 1 0
0 | 0 | 1 | 0 0
0 | 1 | 0 | 1 1
0 | 1 | 1 | 0 0
1 | 0 | 0 | 1 0
1 | 0 | 1 | 0 0
1 | 1 | 0 | 0 0
1 | 1 | 1 | 0 0

## Slide 30: From truth table to a Boolean expression
(x And Not(y) And Not(z))
x | y | z | f
0 | 0 | 0 | 1 0
0 | 0 | 1 | 0 0
0 | 1 | 0 | 1 1
0 | 1 | 1 | 0 0
1 | 0 | 0 | 1 1
1 | 0 | 1 | 0 0
1 | 1 | 0 | 0 0
1 | 1 | 1 | 0 0

## Slide 31: From truth table to a Boolean expression
(Not(x) And Not(y) And Not(z))
(Not(x) And y And Not(z))
(x And Not(y) And Not(z))
x | y | z | f
0 | 0 | 0 | 1 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 32: From truth table to a Boolean expression
(Not(x) And Not(y) And Not(z))
(Not(x) And y And Not(z))
(x And Not(y) And Not(z))
Or
Or
x | y | z | f
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
(Not(x) And Not(y) And Not(z)) Or (Not(x) And y And Not(z)) Or (x And Not(y) And Not(z)) =

## Slide 33: From truth table to a Boolean expression
(Not(x) And Not(y) And Not(z))
(Not(x) And y And Not(z))
(x And Not(y) And Not(z))
Or
Or
x | y | z | f
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
(Not(x) And Not(y) And Not(z)) Or (Not(x) And y And Not(z)) Or (x And Not(y) And Not(z)) =
(Not(x) And Not(z)) Or (x And Not(y) And Not(z)) =
(Not(x) And Not(z)) Or (Not(y) And Not(z)) =
Not(z) And (Not(x) Or Not(y))

## Slide 34: Theorem
Lemma: Any Boolean function can be represented using an expression containing And, Or And Not operations.
Proof:
Use the truth table to Boolean expression method
Lemma: Any Boolean function can be represented using an expression containing And and Not operations.
Proof:
(x Or y) = Not(Not(x) And Not(y))
Can we do better than this?

## Slide 35: ____________
(x _______ y) = Not(x And y)
x | y | Nand
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 36: Theorem (revisited)
Lemma: Any Boolean function can be represented using an expression containing And, Or And Not operations.
Proof:
Use the truth table to Boolean expression method
Lemma: Any Boolean function can be represented using an expression containing And and Not operations.
Proof:
(x Or y) = ___________________
Theorem: Any Boolean function can be represented using an expression containing Nand operations only.
Proof:
Not(x) = (x ________ x)
(x And y) = ______________

## Slide 37: Chapter 1: Boolean logic
  Boolean logic
  Boolean function synthesis
  Hardware description language
  Hardware simulation
  Multi-bit buses
  Project 1 overview

## Slide 38: Building a logic gate
The Process:
Design the gate architecture
Specify the architecture in HDL
Test the chip in a hardware simulator
Optimize the design
Realize the optimized design in silicon.
?
Xor
a
b
out
outputs 1 if one, and only one, of its inputs, is 1.

## Slide 39: Building a logic gate
The Process:
Design the gate architecture
Specify the architecture in HDL
Test the chip in a hardware simulator
Optimize the design
Realize the optimized design in silicon.
?
Xor
a
b
out
outputs 1 if one, and only one, of its inputs, is 1.

## Slide 40: Design: from requirements to interface
a | b | out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Requirement:
Build a gate that delivers this functionality
Xor
a
b
out
outputs 1 if one, and only one, of its inputs, is 1.
/** Xor gate: out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Implementation missing
}
Gate interface
Expressed as an HDL stub file

## Slide 41: Design: from requirements to gate diagram
a
Not
Not
And
And
Or
b
out
General idea:
out=1 when:
a And Not(b)
Or
b And Not(a)
a | b | out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Xor
a
b
out
outputs 1 if one, and only one, of its inputs, is 1.
Requirement:
Build a gate that delivers this functionality

## Slide 42: Design: from gate diagram to HDL
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a
/** Xor gate: out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// implementation missing
}

## Slide 43: Design: from gate diagram to HDL
/** Xor gate: out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (_______________________);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (______________________________________);
}
interface
implementation
Other Xor implementations are possible!
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a

## Slide 44: HDL: some comments
HDL is a functional / declarative language
The order of HDL statements is insignificant
Before using a chip part, you must know its interface. For example:
  Not(in= ,out=), And(a= ,b= ,out= ), Or(a= ,b= ,out= )
Connection patterns like chipName(a=a,…) and chipName(…,out=out) are common
/** Xor gate: out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}

## Slide 45: Hardware description languages
Our HDL
Similar in spirit to other HDLs
Minimal and simple
Provides all you need for this course
Common HDLs:
VHDL
Verilog
Many more HDLs…
  Textbook / Appendix A
  Lecture material / HDL Survival Guide
HDL Documentation:

## Slide 46: Chapter 1: Boolean logic
  Boolean logic
  Boolean function synthesis
  Hardware description language
  Hardware simulation
  Multi-bit buses
  Project 1 overview

## Slide 47: Hardware simulation in a nutshell
Simulation options:
Interactive
Script-based
With / without output and compare files
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
HDL code
load Xor.hdl,
output-file And.out,
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;
test script
simulate
hardware simulator

## Slide 48: Interactive simulation (using Xor as an example)
Simulation process:
Load the HDL file into the hardware simulator
Enter values (0’s and 1’s) into the chip’s input pins (e.g. a and b)
Evaluate the chip’s logic
Inspect the resulting values of:
  Output pins (e.g. out)
  Internal pins (e.g. nota, notb, aAndNotb, notaAndb)
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
Xor.hdl
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}

## Slide 49: Interactive simulation
HDL code
1. manipulate
input pins
3. inspect output pins
4. inspect internal pins
2. evaluate the chip logic

## Slide 50: Script-based simulation
Xor.tst
load Xor.hdl;
set a 0, set b 0, eval;
set a 0, set b 1, eval;
set a 1, set b 0, eval;
set a 1, set b 1, eval;
test script = series of commands to the simulator
Benefits:
“Automatic” testing
Replicable testing
Xor.hdl
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
tested chip

## Slide 51: Script-based simulation, with an output file
The logic of a typical test script
Initialize:
  Load an HDL file
  Create an empty output file
  List the names of the pins whose values will be written to the output file
Repeat:
  set – eval - output
| a | b |out|
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |
Xor.out
Output File, created by the test script as a side-effect of the simulation process
load Xor.hdl,
output-file Xor.out,
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;
Xor.tst
test
script
tested chip
Xor.hdl
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
tested chip

## Slide 52: Script-based simulation
HDL code
test script
inspect the output file
run the script

## Slide 53: Hardware simulators
There are many of them!
Our hardware simulator
Minimal and simple
Provides all you need for this course
Hardware Simulator Tutorial
Hardware simulator documentation:

## Slide 54: Revisiting script-based simulation with output files
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
Xor.hdl
tested chip
load Xor.hdl,
output-file Xor.out,
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;
Xor.tst
test script
| a | b |out|
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |
Xor.out
Output file, created by the test script as a side-effect of the simulation process

## Slide 55: Script-based simulation, with compare files
Simulation-with-compare-file logic
When each output command is executed, the outputted line is compared to the corresponding line in the compare file
If the two lines are not the same, the simulator throws a comparison error.
load Xor.hdl,
output-file Xor.out,
compare-to Xor.cmp,
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;
Xor.tst
| a | b |out|
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |
Xor.out
| a | b |out|
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |
Xor.cmp
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
Xor.hdl
tested chip
test script

## Slide 56: Behavioral simulation
Behavioral simulation:
The chip logic (abstraction) can be implemented in some high-level language
Enables high-level planning and testing of a hardware architecture before writing any HDL code.
load Xor.hdl,
output-file Xor.out,
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;
Xor.tst
test script
CHIP Xor {
IN a, b;
OUT out;
BUILTIN Xor
// Built-in chip implementation,
// can execute in the hardware
// simulator like any other chip.
}
Xor.hdl
built-in chip implementation
| a | b |out|
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |
Xor.out
| a | b |out|
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |
Xor.cmp

## Slide 57: Hardware construction projects
The players (first approximation):
  System architects
  Developers
The system architect decides which chips are needed
For each chip, the architect creates
  A chip API
  A test script
  A compare file
Given these resources, the developers can build the chips.

## Slide 58: The developer’s view (of, say, a Xor gate)
Taken together, the three files provide a convenient specification of:
  The chip interface (.hdl)
  What the chip is supposed to do (.cmp)
  How to test the chip (.tst)
The developer’s task: implement the chip, using these resources.
load Xor.hdl,
output-file Xor.out,
compare-to Xor.cmp
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;
Xor.tst
test script
/** returns 1 if (a != b) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Implementation missing
}
Xor.hdl
stub file
| a | b |out|
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |
Xor.cmp
compare file

## Slide 59: Chapter 1: Boolean logic
  Boolean logic
  Boolean function synthesis
  Hardware description language
  Hardware simulation
  Multi-bit buses
  Project 1 overview

## Slide 60: Arrays of Bits
Sometimes we wish to manipulate an array of bits as one group
It’s convenient to think about such a group of bits as a single entity, sometime termed “bus”
HDLs usually provide notation and means for handling buses.

## Slide 61: Example: adding 16-bit integers
/*
* Adds two 16-bit inputs.
*/
CHIP Add16 {
IN __________, _________;
OUT _____________;
PARTS:
...
}
/*
* Adds three 16-bit inputs.
*/
CHIP Add3Way16 {

## Slide 62: Example: adding 16-bit integers
/*
* Adds two 16-bit values.
*/
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
/*
* Adds three 16-bit inputs.
*/
CHIP Add3Way16 {
IN first[16], second[16], third[16];
OUT out[16];
PARTS:
Add16(a=first, b=second, out=temp);
Add16(a=temp, b=third, out=out);
}

## Slide 63: Working with individual bits within buses
/*
* 4-way And: Ands 4 bits.
*/
CHIP And4Way {

## Slide 64: Working with individual bits within buses
/*
* 4-way And: Ands 4 bits.
*/
CHIP And4Way {
IN a[4];
OUT out;
PARTS:
And(a=a[0], b=a[1], out=_________);
And(a=________, b=a[2], out=t012);
And(a=t012, b=a[3], out=out);
}

## Slide 65: Working with individual bits within buses
/*
* Bit-wise And of two 4-bit inputs
*/
CHIP And4 {

## Slide 66: Working with individual bits within buses
/*
* Bit-wise And of two 4-bit inputs
*/
CHIP And4 {
IN a[4], b[4];
OUT out[4];
PARTS:
And(a=a[0], b=b[0], out=_________);
And(a=a[1], b=b[1], out=out[1]);
And(a=a[2], b=b[2], out=out[2]);
And(a=a[3], b=b[3], out=out[3]);
}

## Slide 67: Sub-buses
Buses can be composed from (and decomposed into) sub-buses
...
IN lsb[8], msb[8], …
...

## Slide 68: Sub-buses
Buses can be composed from (and decomposed into) sub-buses
Some syntactic choices of our HDL
buses are indexed right to left: if foo is a 16-bit bus, then foo[0] is the right-most bit, and foo[15] is the left-most bit
overlaps of sub-buses are allowed in output buses of parts
width of internal pin buses is deduced automatically
The false and true constants may be used as buses of any width.
...
IN lsb[8], msb[8], …
...
Add16(a[0..7]=lsb, a[8..15]=msb, b=…, out=…);
Add16(…, out[0..3]=t1, out[4..15]=t2);
내부핀f 에 대해서
x=f[0..3] 이런 표현은 안됨.
입력핀i에 대해서는
w=i[0..3] 은 됨.
최종 out 핀에 대해서
y=out[0..3] 이런 표현도 안됨

## Slide 69: Chapter 1: Boolean logic
  Boolean logic
  Boolean function synthesis
  Hardware description language
  Hardware simulation
  Multi-bit buses
  Project 1 overview

## Slide 70: Nand to Tetris course methodology
how?
one step at a time
here’s a logic gate, go build computer
Project 1: the first step

## Slide 71: Project 1
Given: Nand
Goal: Build the following gates:
Why these 15 particular gates?
Commonly used gates
Comprise all the elementary logic gates needed to build our computer.
Elementary logic gates
Not
And
Or
Xor
Mux
DMux
Or8Way
Mux4Way16
Mux8Way16
DMux4Way
DMux8Way
Multi-way variants
Not16
And16
Or16
Mux16
16-bit variants

## Slide 72: Project 1
Given: Nand
Goal: Build the following gates:
Elementary logic gates
Not
And
Or
Xor
Mux
DMux
Or8Way
Mux4Way16
Mux8Way16
DMux4Way
DMux8Way
Multi-way variants
Not16
And16
Or16
Mux16
16-bit variants

## Slide 73: Multiplexor
sel | out
0 | a
1 | b
abbreviated truth table
A 2-way multiplexor enables selecting, and outputting, one of two possible inputs
Widely used in:
  Digital design
  Communications networks
a | b | sel | out
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 1 | 1
if (sel==0)
out=a
else
out=b

## Slide 74: Example: using mux logic to build a programmable gate
if (sel==0)
out = (a And b)
else
out = (a Or b)
a | b | sel | out
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1
When sel==0 the gate acts like an And gate
When sel==1 the gate acts like an Or gate
CHIP AndMuxOr {
IN a, b, sel;
OUT out;
Mux.hdl

## Slide 75: Example: using mux logic to build a programmable gate
if (sel==0)
out = (a And b)
else
out = (a Or b)
a | b | sel | out
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1
When sel==0 the gate acts like an And gate
When sel==1 the gate acts like an Or gate
CHIP AndMuxOr {
IN a, b, sel;
OUT out;
PARTS:
And (a=a, b=b, out=andOut);
Or (a=a, b=b, out=orOut);
Mux (a=andOut, b=orOut, sel=sel, out=out);
}
Mux.hdl

## Slide 76: Multiplexor implementation
sel | out
0 | a
1 | b
Implementation tip:
Can be implemented with And, Or, and Not gates
CHIP Mux {
IN a, b, sel;
OUT out;
PARTS:
// Put your code here:
}
Mux.hdl
if (sel==0)
out=a
else
out=b

## Slide 77: Demultiplexor
in | sel | a | b
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
if (sel==0)
{a,b}={in,0}
else
{a,b}={0,in}
CHIP DMux {
IN in, sel;
OUT a, b;
PARTS:
// Put your code here:
}
DMux.hdl
Acts like the “inverse” of a multiplexor
Distributes the single input value into one of two possible destinations

## Slide 78: Example: Multiplexing / demultiplexing in communications networks
Each sel bit is connected to an oscillator that produces a repetitive train of alternating 0 and 1 signals
Enables transmitting multiple messages on a single, shared communications line
A common use of multiplexing / demultiplexing logic
Unrelated to this course.
source
destination

## Slide 79: Project 1
Elementary logic gates
Not
And
Or
Xor
Mux
DMux
Or8Way
Mux4Way16
Mux8Way16
DMux4Way
DMux8Way
Multi-way variants
Not16
And16
Or16
Mux16
16-bit variants

## Slide 80: And16
A straightforward 16-bit extension of the elementary And gate
(See previous slides on working with multi-bit buses)
CHIP And16 {
IN a[16], b[16];
OUT out[16];
PARTS:
// Put your code here:
}
out = 0 0 1 0 1 0 0 1 0 0 0 0 1 0 0 0
a = 1 0 1 0 1 0 1 1 0 1 0 1 1 1 0 0
b = 0 0 1 0 1 1 0 1 0 0 1 0 1 0 1 0

## Slide 81: Project 1
Elementary logic gates
Not
And
Or
Xor
Mux
DMux
Or8Way
Mux4Way16
Mux8Way16
DMux4Way
DMux8Way
Multi-way variants
Not16
And16
Or16
Mux16
16-bit variants

## Slide 82: 16-bit, 4-way multiplexor
sel[1] | sel[0] | out
0 | 0 | a
0 | 1 | b
1 | 0 | c
1 | 1 | d
Implementation tip:
Can be built from several Mux16 gates
CHIP Mux4Way16 {
IN a[16], b[16], c[16], d[16],
sel[2];
OUT out[16];
PARTS:
// Put your code here:
}
Mux4Way16.hdl

## Slide 83: Project 1
So how to actually build these gates?
Elementary logic gates
Not
And
Or
Xor
Mux
DMux
Or8Way
Mux4Way16
Mux8Way16
DMux4Way
DMux8Way
Multi-way variants
Not16
And16
Or16
Mux16
16-bit variants
Given: Nand
Goal: Build the following gates:

## Slide 84: Chip building materials (using Xor as an example)
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Put your code here.
}
Xor.hdl
a b out
0 0 0
0 1 1
1 0 1
1 1 0
Xor.cmp
load Xor.hdl,
output-file Xor.out,
compare-to Xor.cmp,
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;
Xor.tst
When running your Xor.hdl on the supplied Xor.tst, your Xor.out should be the same as the supplied Xor.cmp
The contract:
Xor
a
b
out
outputs 1 if a != b

## Slide 85: Project 1 Resources
www.nand2tetris.org
All the necessary project 1 files are available in:
nand2tetris/projects/01

## Slide 86: More resources
Text editor (for writing your HDL files)
HDL Survival Guide
Hardware Simulator Tutorial
nand2tetris Q&A forum
All available in: www.nand2tetris.org

## Slide 87: Hack chipset API
a
Not
Not
And
And
Or
b
out
out
b
a
b
a
in
in
out
out
out
out
b
a
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in= , out=);
Not (in= , out=);
And (a= , b= , out=);
And (a= , b=b , out=);
Or (a= , b= , out=);
}
When deciding to use some chip-parts, how do I know the names of their input and output pins?

## Slide 88: Hack chipset API
Add16 (a= ,b= ,out= );
ALU (x= ,y= ,zx= ,nx= ,zy= ,ny= ,f= ,no= ,out= ,zr= ,ng= );
And16 (a= ,b= ,out= );
And (a= ,b= ,out= );
Aregister (in= ,load= ,out= );
Bit (in= ,load= ,out= );
CPU (inM= ,instruction= ,reset= ,outM= ,writeM= ,addressM= ,pc= );
DFF (in= ,out= );
DMux4Way (in= ,sel= ,a= ,b= ,c= ,d= );
DMux8Way (in= ,sel= ,a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= );
Dmux (in= ,sel= ,a= ,b= );
Dregister (in= ,load= ,out= );
FullAdder (a= ,b= ,c= ,sum= ,carry= );
HalfAdder (a= ,b= ,sum= , carry= );
Inc16 (in= ,out= );
Keyboard (out= );
Memory (in= ,load= ,address= ,out= );
Mux16 (a= ,b= ,sel= ,out= );
Mux4Way16 (a= ,b= ,c= ,d= ,sel= ,out= );
Mux8Way16 (a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= ,sel= ,out= );
Mux8Way (a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= ,sel= ,out= );
Mux (a= ,b= ,sel= ,out= );
Nand (a= ,b= ,out= );
Not16 (in= ,out= );
Not (in= ,out= );
Or16 (a= ,b= ,out= );
Or8Way (in= ,out= );
Or (a= ,b= ,out= );
PC (in= ,load= ,inc= ,reset= ,out= );
PCLoadLogic (cinstr= ,j1= ,j2= ,j3= ,load= ,inc= );
RAM16K (in= ,load= ,address= ,out= );
RAM4K (in= ,load= ,address= ,out= );
RAM512 (in= ,load= ,address= ,out= );
RAM64 (in= ,load= ,address= ,out= );
RAM8 (in= ,load= ,address= ,out= );
Register (in= ,load= ,out= );
ROM32K (address= ,out= );
Screen (in= ,load= ,address= ,out= );
Xor (a= ,b= ,out= );
(see HDL Survival Guide @ www.nand2tetris.org)

## Slide 89: Built-in chips
CHIP Foo {
IN ...;
OUT ...;
PARTS:
...
Mux16(...)
...
}
Q: What happens if there is no Mux16.hdl file in the current directory?

## Slide 90: Built-in chips
CHIP Foo {
IN ...;
OUT ...;
PARTS:
...
Mux16(...)
...
}
The supplied simulator software features built-in chip implementations of all the chips in the Hack chip set
If you don’t implement some chips from the Hack chipset, you can still use them as chip-parts of other chips:
  Just rename their given stub files to, say, Mux16.hdl1
  This will cause the simulator to use the built-in chip implementation.
Q: What happens if there is no Mux16.hdl file in the current directory?
A: The simulator invokes, and evaluates, the built-in version of Mux16 (if such exists).

## Slide 91: Best practice advice
Try to implement the chips in the given order
If you don’t implement some chips, you can still use them as chip-parts in other chips (the built-in implementations will kick in)
You can invent new, “helper chips”; however, this is not required: you can build any chip using previously-built chips only
Strive to use as few chip-parts as possible.

## Slide 92: Chapter 1: Boolean logic
  Boolean logic
  Boolean function synthesis
  Hardware description language
  Hardware simulation
  Multi-bit buses
  Project 1 overview